## Slide 1
BIM472 IMAGE PROCESSING — PROJECT 2
ÇAĞDAŞ KAPLAN
MERT CAN KALINLIOĞLU
:
OPTIC DISC & FOVEA LOCALIZATION

## Slide 2
Main goal
  Detect optic disc center
  Segment optic disc region
  Locate fovea center
  Compare predictions with ground truth
Why these landmarks?
  They are basic anatomical reference points
  They help define retinal regions of interest
  They support later diagnosis-oriented processing
  They make algorithm outputs measurable

## Slide 3
01 - INPUT IMAGE
End to End Pipeline
02 - PREPROCESSING
03 - OD DETECTION
04 - OD SEGMENTATION
05 - FOVEA LOCALIZATION
06 - EVALUATION

## Slide 4
PREPROCESSING PIPELINE
Green channel → CLAHE → Median fIlter → SegmentatIon mask

## Slide 5
Optic Disc Detection & Segmentation
Algorithm logic
  Use red channel for bright OD search
  Mask black background / field-of-view edges
  Apply strong Gaussian blur to suppress vessels and lesions
  Pick brightest location as OD center
  Segment local ROI using Otsu + morphology

## Slide 6
Fovea Localization
How it works
  Use detected OD center as anchor
  Decide left/right eye by OD position
  Create a horizontal search window
  Blur the search region aggressively
  Remove unsafe edge areas using FOV mask
  Select the darkest point as fovea center

## Slide 7
Visual Results Gallery
How to read the examples
  Left side: original fundus image with ground truth and predicted centers.
  Right side: preprocessed image with detected centers.
  Close OD GT and OD Pred markers indicate successful optic disc localization.
  Fovea can be more sensitive to lesions and low contrast.

## Slide 8
A MORE CHALLENGING EXAMPLE
Observation 1
OD is still easier because it is a bright anatomical structure.
Observation 2
Dark lesions or low contrast can confuse darkest-point fovea search.
Takeaway
The method is explainable, but rule-based localization has limits.

## Slide 9
LOCALIZATION PERFORMANCE
172 PX
Mean OD error
259 PX
Mean fovea error
90.3%
OD ≤ 200 px
64.2%
Fovea ≤ 100 px

## Slide 10
OD Segmentation Performance
Result interpretation
  Mean recall is high (~0.713): the OD region is often covered.
  Mean precision is lower (~0.191): masks can include false positives.
  Mean F-score / Dice is ~0.286 and mean IoU is ~0.181.
  Center localization is stronger than exact boundary extraction.

## Slide 11
Image Processing Techniques Used
Color space
RGB channels, green-channel extraction
Enhancement
CLAHE, illumination handling
Filtering
Gaussian blur, median filter
Morphology
Closing, hole filling, connected components
Thresholding
Percentile threshold, Otsu threshold
Evaluation
Distance error, Precision, Recall, Dice, IoU

## Slide 12
Limitations & Future Work
Current limitations
  OD boundaries are not always precise
  Fovea localization is sensitive to lesions and low contrast
  Hand-crafted thresholds may not generalize perfectly
  Very bright lesions can affect OD segmentation
Future improvements
  Adaptive ROI refinement
  Better vessel / lesion suppression
  Contour-based boundary correction
  Comparison with learning-based baselines
  Parameter tuning per image quality
Conclusion
  The project demonstrates that an explainable classical pipeline can localize key retinal landmarks, especially optic disc center, while revealing the limitations of rule-based segmentation and fovea estimation.

## Slide 13
THANK YOU FOR LISTENING